Hydrous olivine defect reactions

# List of defects
Description	Label	Kroger-Vink	Formula	Peak (cm-1)
Ti on an M site, likely M1, a Si vacancy and ferric iron	[Ti-anhyd]	{Ti**M1 – V’’’’Si – 2(Fe3+)*M}	MgTiFe2SiO8	None
Titanium clinohumite. See, e.g., Walker et al. 2007	[Ti-2H]	{Ti**M1-V’’’’Si-2(OH)*O}	MgTiH2O4	3525, 3573
A Si vacancy and 4H+	[Si-4H]	{V’’’’Si-4(OH)*O}	Mg2H4O4	3600
A Si vacancy and 4 ferric irons on M sites	[Si-anhyd]	{V’’’’Si-4(Fe3+)*M}	Fe4SiO8	None
A Si vacancy, 2H+, and 2 ferric irons on M sites	[Si-2H]	{V’’’’Si-2(Fe3+)*M-2(OH)*O}	Fe2H2O4	3600
A metal vacancy, a ferric iron on an M site, and H+	[tri-H]	{V’’M-(Fe3+)*M-(OH)*O}	FeHSiO4	3356
A metal vacancy and 4 ferric irons on M sites	[tri-anhyd]	{V’’M-2(Fe3+)*M}	MgFe2Si2O8	None­

# Fast diffusion in and out (decoration of pre-existing Ti defects)
## Overview
[Ti-anhyd] + H2 = [Ti-2H]
## Kroger-Vink
{Ti**M1 – V’’’’Si – 2(Fe3+)*M} + H2 = {Ti**M1-V’’’’Si-2(OH)*O} + 2FexM

## Formula
MgTiFe2SiO8 + H2 = MgTiH2O4 + Fe2SiO4

# Slow redistribution of H between Si vacancies
## Overview
[Ti-anhyd] + [Si-4H] → [Ti-2H] + [Si-2H]
## Kroger-Vink
{Ti**M1 – V’’’’Si – 2(Fe3+)*M} + {V’’’’Si-4(OH)*O} → {Ti**M1-V’’’’Si-2(OH)*O} + {V’’’’Si-2(Fe3+)*M-2(OH)*O}

## Formula
MgTiFe2SiO8 + Mg2H4O4 → MgTiH2O4 + Fe2H2O4 + Mg2SiO4
## Alternative: full dehydration of [Si]
2[Ti-anhyd] + [Si-4H] → 2[Ti-2H] + [Si-anhyd]

# Redistribution of H in Kilauea Iki at 800C
## Overview
[Si-anhyd] + 4[tri-H] → [Si-4H] + 4[tri-anhyd]
## Kroger-Vink
{V’’’’Si-4(Fe3+)*M} + 4{V’’M-(Fe3+)*M-(OH)*O}→ {V’’’’Si-4(OH)*O} + 4{V’’M-2(Fe3+)*M}
## Formula
Fe4SiO8 + 4FeHSiO4 + 3Mg2SiO4 → Mg2H4O4 + 4MgFe2Si2O8